## Slide 1: Data Conversions
ASCII to BCD/Hexadecimal
BCD/Hexadecimal to ASCII
8 bit BCD to Hexadecimal
8 bit Hexadecimal to BCD.

## Slide 2: 1. ASCII to BCD/HEXA… (Used to read numbers(BCD/HEXA) from keyboard)

## Slide 3
ASCII | HEX | SYMBOL
48 | 30H | 0
49 | 31H | 1
50 | 32H | 2
51 | 33H | 3
52 | 34H | 4
53 | 35H | 5
54 | 36H | 6
55 | 37H | 7
56 | 38H | 8
57 | 39H | 9
65 | 41H | A
66 | 42H | B
67 | 43H | C
68 | 44H | D
69 | 45H | E
70 | 46H | F

## Slide 4: Converting 2 ASCII codes to BCD
Convert first ASCII number to unpacked BCD
Convert second ASCII number to unpacked BCD
Move first BCD nibble to upper nibble position in byte
Pack two BCD nibbles in one byte

## Slide 5: Example…
MOV BL, ‘5’ ; ASCII OF ‘5’ (35H)
MOV AL, ‘9’ ; ASCII OF ‘9’ (39H)
AND BL, 0FH ; NOW BL=05H
AND AL, 0FH ; NOW AL=09H
MOV CL, 04H
SHL BL, CL ; NOW BL=50H
OR AL, BL ; NOW AL=59H
;Otherwise ADD AL, BL

## Slide 6: Reading 2 digit (8-bit) BCD number from keyboard and store in AL…
MOV AH, 01H
INT 21H
MOV CL, 04
SHL AL, CL
MOV BL, AL
MOV AH, 01H
INT 21H
AND AL, 0FH
ADD AL, BL

## Slide 7: Reading 2 digit (8-bit) HEXA number from keyboard and store in AL…
MOV AH, 01H
INT 21H
CMP AL, 39H
JBE L1
ADD AL, 09H
L1:
MOV CL, 04
SHL AL, CL
MOV BL, AL
MOV AH, 01H
INT 21H
CMP AL, 39H
JBE L2
ADD AL, 09H
L2:
AND AL, 0FH
ADD AL, BL

## Slide 8: 2. BCD/HEXA to ASCII… (Used to display numbers(BCD/HEXA))

## Slide 9: Displaying a 2 digit (8-bit) BCD number which is stored in BL…
MOV DL, BL
MOV CL, 04
SHR DL, CL
ADD DL, 30H
MOV AH, 02H
INT 21H
MOV DL, BL
AND DL, 0FH
ADD DL, 30H
MOV AH, 02H
INT 21H

## Slide 10: Displaying a 2 digit (8-bit) HEXA number which is stored in BL…
MOV DL, BL
MOV CL, 04
SHR DL, CL
CMP DL, 09H
JBE L1
ADD DL, 07H
L1:
ADD DL, 30H
MOV AH, 02H
INT 21H
MOV DL, BL
AND DL, 0FH
CMP DL, 09H
JBE L2
ADD DL, 07H
L2:
ADD DL, 30H
MOV AH, 02H
INT 21H

## Slide 11: Assignment…
Read a 8 bit BCD value from keyboard and display
Read a 8 bit HEXA value from keyboard and display
Linear Search/Binary Search – Display the position where element is found
Finding max/min in array – Display the max/min number

## Slide 12: 3. 8 bit BCD to Binary(Hexa)…

## Slide 13
bcdinput db 17
binval db ?
MOV BL, bcdinput
AND BL,0FH ; BL=07h(1st digit)
MOV AL, bcdinput
AND AL,0F0H
MOV CL,04H
SHR AL,CL ; AL=01h(2nd digit)
MOV BH,0AH
MUL BH
ADD AL,BL ;AL=11H(hex of 17)
MOV binval, AL

## Slide 14: 4. 8 bit Binary(Hexa) to BCD…

## Slide 15
Bin db 17H
Dec_val db 00h
MOV CH,00H
MOV AL, Bin ; AL=17H
MOV BL,0AH
UP: CMP CH,02H
JZ EXIT
MOV AH,00H
DIV BL ; AH IS REMINDER, AL IS QUOTIENT
ADD dec_val,AH
MOV CL,04H
ROR dec_val,CL
INC CH
JMP UP

## Slide 16: Assignments…
Convert 16 bit BCD to Binary(Hexa)
Convert 16 bit Binary(Hexa) to BCD